## Slide 1: End-to-End Quadrotor Position Control via Proximal Policy Optimization with Direct Motor Actuation
Adrian Ferdinand Jotham, Muhammad Wicaksono, Soo Young Shin
Dept. IT Convergence Engineering
Kumoh National Institute of Technology

## Slide 2: Introduction & Contributions
Classical control: 4 tuned layers (planner → position → attitude → motor mixer), each brittle to unmodelled dynamics.
RL collapses all layers into one neural network — sensors map directly to motor commands.
Direct-RPM is the hardest variant: every layer must be learned from one reward signal.
1. Reward Design
Potential-based approach term gives a dense transit gradient toward the goal.
Velocity-gated hover bonus rewards arrival without overshoot.
2. Training Progression
Training from 3M → 40M environment steps.
Two spawn regimes: clean-start and full curriculum randomisation.
3. Robustness Gap
Distance-stratified success rates show graceful degradation with target distance.
Robustness gap narrows monotonically: 47.1 → 28.3 pp.
4. Open Environment
Open Crazyflie 2.x training environment.
Newton GPU physics + Stable-Baselines3 PPO.

## Slide 3: System Comparison
NEURAL NETWORK
Multi Layer Perceptron (22 x 128 x 128 x 4)
Sensors
Position & Attitude Estimator
Position Controller
Classical Control Architecture
End to End Control Architecture
Attitude & Rate Controller
Mixer
Navigator
Actuator
Src : PX4 Flight Stack

## Slide 4: Method
End-to-end: obs → PPO → motor RPM.
Shared 2 × 256 MLP, actor + critic heads.
Simulation Environment
100 Hz Newton GPU integration.
Motor lag τ = 0.15 s (1st-order LPF).
16 parallel envs.
Episodes ≤ 800 steps (8 s).
Network Architecture
PPO Configuration
SB3 PPO, MLP 2 × 256 (tanh).
Rollout 2,048; batch 64.
γ = 0.99, λ = 0.95.
clip = 0.2, ent = 0.005.
Table 1. Crazyflie 2.x Parameters
Parameter | Value
Mass | 27 g
Arm length | 32.5 mm
Ixx = Iyy | 1.657 × 10−5 kg·m2
Izz | 2.900 × 10−5 kg·m2
KT (thrust) | 3.16 × 10−10 N / RPM2
KD (drag) | 7.94 × 10−12 N·m / RPM2
Hover RPM | ≈ 14,476 RPM
Observation (22D)
Linear 256 + tanh
Linear 256 + tanh
Actor (4D) | Critic V(s)
Proximal Policy Optimization
Goal: π* = arg max π 𝔼π [ Σt γt rt ]
Loss: LCLIP(θ) = 𝔼t [ min ( rt(θ) Ât , clip( rt(θ), 1 − ε, 1 + ε) Ât ) ]
Clipping bounds the policy step — the same rollout can be reused safely.

## Slide 5: Reward Function & Spawn Curriculum
Term | Formula | Role
pos_c | −Crp · ‖perr‖2 | Position precision
orient_c | −Crq · (1 − qw2) | Upright attitude
vel_c | −Crv · ‖v‖2 | Velocity damping
ang_c | −Crω · ‖ω‖2 | Angular stability
act_c | −Cra · ‖Δa‖2 | Action jerk penalty
survival | +0.50 (fixed) | Stay airborne
approach | +λ · (dt−1 − dt), d > 0.10 m | Dense transit signal
hover_bonus | +0.15, d < 0.15 m & ‖v‖ < 0.5 | Settlement reward
arrival | +15.0 (one-time) | Waypoint reached
crash | −2.0 (one-time) | Ground impact
Why these terms
Penalties (pos / orient / vel / ang / act) shape the long-tail target hovering behaviour.
Approach term gives a dense gradient — pure goal-reach is too sparse for PPO.
Velocity-gated hover bonus prevents the policy from sprinting at the target.
Arrival (+15) and crash (−2) provide the terminal signal.
Curriculum logic
c ∈ [0, 1] ramps spawn difficulty over the first 1.5 M steps.
Reward weights anneal in parallel — learn to hover first, then to recover.

## Slide 6: Results
How we measure it
A leg = one waypoint segment. Success = ‖perr‖ < 0.15 m.
Multi-waypoint chaining, no reset, 8 000-step budget, 20 episodes.
Key findings
Clean-start: 73 → 82.9% (3 → 30 M). Converges at ~30 M.
Randomised keeps improving: 25.9 → 53.5%.
Robustness gap narrows monotonically: 47.1 → 28.3 pp.
Distance-stratified: 100% at < 0.5 m drops to 68.2% at 1.5–3.0 m.
Chart: Per-Leg Waypoint Success Rate (%)
| 3M | 30M | 40M
Clean-start | 73 | 82.9 | 81.8
Randomised | 25.9 | 42.9 | 53.5

## Slide 7: Conclusion & Future Work
End-to-end PPO learned direct-RPM position control — no hand-tuned cascade.
Robustness keeps improving past clean-start convergence.
Sim-to-Real
Validate the simulator: zero-shot transfer to a physical Crazyflie 2.x.
Real motor lag and battery sag will stress the policy.
Motor-Lag Robustness
Randomise τ around 0.15 s during training.
Closes the gap between sim motor dynamics and any unseen real airframe.
Reward Refinement
Remove flat +0.5 survival bonus — currently creates a hover attractor away from the goal.
Replace with a small altitude/recovery term.